## Slide 1: METAL SHOP SAFETY
IF YOU CAN’T BE SAFE, YOU CAN’T BE HERE

## Slide 2: BEHAVIOUR
NO HORSEPLAY
NO ROUGH-HOUSING
NO RUNNING
8

## Slide 3: BEHAVIOUR
NO UNNECESSARY NOISE
  We need to hear what’s going on
  Machines: “good” sounds and “bad” sounds
PAY ATTENTION TO OTHERS
  They might not pay attention to you
8

## Slide 4: ATTIRE
NO JEWELRY
  Rings, bracelets, necklaces,
  ties, etc.
NO LOOSE CLOTHING
  Hoodie strings, baggy clothes, earphones, etc
8

## Slide 5: ATTIRE
NO LONG HAIR
  Tie it back
WEAR NATURAL FIBER
CLOTHING
  Cotton, leather, etc.
8

## Slide 6: PROCEDURAL
WORK CLEAN & HELP CLEAN
  A clean shop is a safe shop
NO DISTRACTIONS
  iPod, daydreaming, under influence of…?
8

## Slide 7: PROCEDURAL
ASK FOR HELP or DEMOS
  I love the “teaching” part of my job
LOCKOUT or UNPLUG the machine when making adjustments
  No accidental “turn on”
8

## Slide 8: PROCEDURAL
STAND AN ARM’S LENGTH AWAY
  If the operator could punch you, you’re too close, give them room
KEEP FINGERS A HAND WIDTH’S AWAY FROM CUTTERS
  “No Finger Zone”
8

## Slide 9: SAFETY EQUIPMENT
THE #1 MOST IMPORTANT:
EYE PROTECTION
  Cutting, striking, shaping or
  removing metal
8

## Slide 10: SAFETY EQUIPMENT
HAND PROTECTION
  Risk of burns or cuts
  Don’t get them wet! (wrecks them)
  Don’t pick up hot metal! (wrecks them)
EAR PROTECTION
  Near loud noises
  If you have to raise your voice,
  you need ear protection
8

## Slide 11: TOOLS

## Slide 12: AVIATION SNIPS
For cutting SHEET METAL only! (it shears)
  Serrated teeth
  Green Cuts Left
  Yellow Cuts Straight
  Red Cuts Right
8

## Slide 13: SIDE CUTTERS
AKA “Diagonal Pliers”
For cutting ROUND material (it pinches)

## Slide 14: VISE
For CLAMPING your project
JAWS will damage your project
  Use SOFT metal to protect YOUR project
8

## Slide 15: ANVIL
For SUPPORTING or SHAPING metal
  Best for Center-Punching

## Slide 16: BALL PEEN HAMMER
For SHAPING and STRIKING
WEAR EYE PROTECTION
  Hardened steel (DO NOT STRIKE TWO HAMMERS TOGETHER)
8

## Slide 17: CROSS PEEN HAMMER
WEAR EYE PROTECTION
Pointy end used to widen metal in Blacksmithing

## Slide 18: FOOT SHEAR
For cutting SHEET METAL ONLY
NO ROUND!!!
8

## Slide 19: JEWELRY SAW
BABY the blade
  Be VERY gentle!
Teeth point TOWARD the handle

## Slide 21: FILE
For SHAPING metal
EASILY dulled, chipped or broken!
  Be GENTLE!!!
  DO NOT bang together or against anything
  Works on PUSH stroke only
8

## Slide 22: HAND DRILL & DRILL PRESS
Makes holes
Wear EYE PROTECTION
All material must be CLAMPED DOWN
8

## Slide 23: HAND DRILL & DRILL PRESS
All holes must be CENTER-PUNCHED
Any hole bigger than 1/4” must be PRE-DRILLED With a smaller drill bit
8

## Slide 24: BUFFING WHEEL
For ART METAL CLASS only
Wear EYE PROTECTION
Polish on BOTTOM of wheel
(Top spins towards you)
8
CAUTION: Polishing gets HOT!
NO CHAINS!

## Slide 25: LATHE
8

## Slide 26: LATHE
Makes things ROUND
Wear EYE PROTECTION
Keep hands, arms, sleeves, hoodie strings THE HELL AWAY from the spinning chuck
It WILL mess you up
8
Notes: Kid in Vernon. Lathe RIPPED his shirt off his body, and was pulling him in by the collar. His face was AT his work in SECONDS by the time the teacher got the power shut off.

## Slide 27
8

## Slide 28: LATHE
Be nice to the cutter – take BABY cuts
NEVER leave the CHUCK KEY in the CHUCK
Spin the chuck BY HAND before you turn it on
8

## Slide 29: LATHE
Cutter should be ~90° to direction of travel
Cutting tip should be same height as project center
8

## Slide 30: MILLING MACHINE
Makes things FLAT
Wear EYE PROTECTION
8

## Slide 31: MILLING MACHINE
Material MUST be WELL CLAMPED
Keep hands, arms, sleeves, hoodie strings THE HELL AWAY from the spinning cutter
  It WILL mess you up
8

## Slide 32: MILLING MACHINE
Cut AGAINST the rotation of the cutter
Be nice to the cutter – take light cuts (Chip Colour!)
8

## Slide 33: BLACKSMITH FORGE
HOT!
FACE SHIELD!
EAR PROTECTION!
LEATHER GLOVES!
LEATHER JACKET
BRAINS
  There’s a story behind that….