## Slide 1: HAND TOOLS

## Slide 3: HAMMERS
Used for striking, riveting, and gasket cutting
Wear eye protection

## Slide 4: HAMMERS
Plastic, lead and rubber mallets are used to prevent damaging the surface

## Slide 5: CHISELS
Used for cutting off rivet heads, bolts and rusted nuts

## Slide 6: PUNCHES
Center Punch
  Preps for drills
Pin Punch
  Removes pins
Drift Punch
  Aligns holes
Taper Punch
  For hitting

## Slide 7: PUNCHES
A Center Punch is needed to mark material before drilling

## Slide 8: PUNCHES
Aside from sharpening, the ends need to be chamfered as they are used

## Slide 9: FILES
Used to shape and smooth material
Single (smooth) or Double cut (rough)
Always use a handle

## Slide 10: HACKSAWS
Used to cut tubing, bolts, other materials
Let the saw do the work

## Slide 11: VISE
A bench mounted clamp

## Slide 12: CLEANING TOOLS
Wire Brushes and Gasket Scrapers
Wear eye protection!

## Slide 13: CLEANING TOOLS
Solvent Tank
Wear eye protection!
Wear rubber gloves!

## Slide 15: SCREWDRIVERS
Flat blade
Philips
Robertson
Torx
Clutch
Do not use as a pry bar
  Instead, use a pry bar

## Slide 16: SLIP JOINT PLIERS
Two sizes of adjustability

## Slide 17: WATER PUMP PLIERS
Five or so sizes of adjustability
“Channel-Lock” is a brand name

## Slide 18: NEEDLE NOSE PLIERS
Great for grabbing or holding small clips or pins
Also has a small wire cutter

## Slide 19: SIDE CUTTERS
Also called Diagonal Pliers
For cutting ROUND

## Slide 20: SNAP RING PLIERS
Internal or External

## Slide 21: LOCKING PLIERS
“Vice Grip” is a brand name

## Slide 22: WRENCHES
Open End
Box End
Combination End
Flare Nut Wrench

## Slide 23: SOCKETS
Fastest and most convenient
6-point and 12-point
Deep-well and standard (shallow) depth

## Slide 24: SWIVEL SOCKETS
Allows the user to turn fastener at an angle
Universal Joint has no socket

## Slide 25: SPEED HANDLE
Allows faster removal/installation

## Slide 26: BREAKER BAR
THIS IS THE TOOL YOU WANT
Also called a Flex-Bar
Allows considerable leverage

## Slide 27: RATCHET HANDLE
Ratcheting mechanism inside allows rapid use in a confined space

## Slide 28: EXTENSIONS
Allows a longer reach
CAUTION: extensions “flex”, reducing force

## Slide 29: REMOVING BROKEN BOLTS
Broken fasteners is a FACT OF LIFE
Try to avoid breaking the fastener in the first place:
  Turn the correct direction
  Penetrating oil
  Heat
  Tapping with hammer
When a fastener breaks, there are ways of dealing with it. Try the easiest fixes first….

## Slide 30: REMOVING BROKEN BOLTS

## Slide 31: REMOVING BROKEN BOLTS

## Slide 32: REMOVING BROKEN BOLTS

## Slide 34: FIXING DAMAGED THREADS
Reality 1: When a threaded hole becomes stripped or damaged (usually aluminum threads)
Reality 2: When removing or drilling out a broken fastener goes horribly wrong
“Heli-Coil” to the rescue
  (but they’re not cheap)

## Slide 35: FIXING DAMAGED THREADS

## Slide 36: FIXING DAMAGED THREADS

## Slide 38: ADJUSTABLE WRENCHES
DO NOT use these.
DO NOT use these.

## Slide 39: CHAIN WRENCH
Greatest tool ever made

## Slide 40: ALLEN WRENCHES
Used for set screws and cap screws

## Slide 41: IMPACT DRIVER
Greatest tool ever made
Loosens the impossible (with a hammer)
Wear eye protection

## Slide 43: FLOOR JACK AND STANDS
SPECIFIC “jacking points”
ALWAYS use jack stands
ALWAYS raise jack handle

## Slide 45: ENGINE CRANE
AKA “Cherry Picker”
Lifts engines out of vehicles
Chain must be WELL secured
NEVER go under an engine supported only by a chain

## Slide 46: OIL DRAIN
Stores drained engine or transmission oil
Must be emptied frequently

## Slide 47: GREASE GUN
Used to lubricate steering and supension components through grease fittings

## Slide 48: GEAR PULLER
Used to remove gears and pulleys
NOT for harmonic balancers

## Slide 49: HARMONIC BALANCER PULLER

## Slide 51: PISTON RING PLIERS
Used to remove/install piston rings from pistons without breaking them

## Slide 53: CYLINDER HONE
Used to remove glazing from cylinders in preparation for new rings
Used with a hand drill and honing oil
Flex Hone (top)
Ball Hone (bottom)

## Slide 55: PISTON RING COMPRESSOR
Compressing piston rings into the ring grooves to fit pistons into the cylinders
Sharp edges may cut hands

## Slide 57: TIRE INFLATOR
Used to inflate tires
Has a built-in pressure gauge

## Slide 58: SPARK PLUG BOOT PLIERS
Removes stubborn and hard to reach spark plug boots

## Slide 59: BATTERY CLAMP PULLER
Removes battery cable clamps without damage

## Slide 60: BATTERY POST CLEANER
Two wire brushes help to clean both battery posts and battery clamps

## Slide 61: TORQUE WRENCH
A tool that allows a MEASURED amount of TIGHTNESS
NOT A BREAKER BAR!
NOT FOR “REMOVING” FASTENERS
  This ruins the calibration

## Slide 62: BEAM TORQUE WRENCH
Has a handle (that flexes) and a needle (that points to numbers)

## Slide 63: MICROMETER TORQUE WRENCH
Dial up desired torque by turning the handle
Lock it
Hear/feel “click”

## Slide 65: TEST LIGHT
“Idiot Light”
Tests electrical circuits
Handle lights up when voltage is present
DO NOT use with computer-controlled components

## Slide 66: DO NOT use this to test computer components

## Slide 67: VALVE SPRING COMPRESSOR
Used for disassembling Cylinder Heads
This type requires cylinder head removal

## Slide 69
Screw head shapes?
Push or pull the wrench?